## Slide 1
ccam-sunrise-project.eu
Welcome to
SUNRISE Workshop 8
For members of the SUNRISE Expert Platform
27 November 2024
Stefan de Vries - Applus IDIADA
Jason Zhang - Warwick University
John Fredrik Grönvall - Chalmers Industriteknik
Industry engagement
Starts at
13:00 CET!
Notes: Hello, my name is … and I work for … where I fulfill the role of …
In this workshop, I will give you a high-level introduction to the SUNRISE Project.

## Slide 2
Welcome
Workshop details
Timeframe 27 November from 13:00 to 14:45 CET
Today’s subject Industry engagement
Goal Increase focus on SAF users in the industry (OEMs and TIER1s)
Workshop team
Organization
Moderation
Julie Castermans [JC]
ERTICO
Stefan de Vries [SV]
IDIADA
Task 2.2 Leader
Jordi Pont [JP]
IDIADA
John Fredrik Grönvall [JfG]
Chalmers Industriteknik
Work Package 2 Leader
Jason Zhang [JZ]
Warwick University

## Slide 3
Workshop and webinars
Expert Platform (EP)
Type: Workshops
Attendants: EP members only
Tools: Teams, Cooperation Platform
Wider public and CCAM Community
Type: Webinars
Attendants: wider public and CCAM community
Tools: Teams
Dialogue
Monologue

## Slide 4
Comments
External CCAM experts are encouraged to provide feedback
On personal behalf. NOT on behalf of your organization.
SUNRISE partners are encouraged to listen and facilitate discussion
All feedback via Cooperation Platform (on SUNRISE website)
On Cooperation Platform, look for questions marked with “[WS8]”
Each workshop will be recorded:
  Presentations will be published
  Discussions will not be published (for internal reference only)
Workshop presentations will be shared afterwards
Questions can be asked in Q&A section, or by raising your (virtual) hand
Say cheese!
Join our
Expert Platform!
ccam-sunrise-project.eu/register

## Slide 5
Agenda
13:00 Welcome & SUNRISE project introduction [by SV]
13:10 SUNRISE Safety Assurance Framework [by JfG & JZ]
13:35 Questions from audience
13:45 SUNRISE Cooperation Platform [by SV]
13:55 Cooperation Platform (CP) Questions [by SV]
14:35 Closing remarks
14:45 Workshop close

## Slide 6: SUNRISE project introduction
27 November 2024
Stefan de Vries - Applus IDIADA
ccam-sunrise-project.eu
Notes: Hello, my name is … and I work for … where I fulfill the role of …
With this presentation, I will give you a high-level introduction to the SUNRISE Project.
But before we start, let me provide you with some context, in order to better understand the reasons for undertaking the SUNRISE project...
The context of the SUNRISE project is safety assurance of automated vehicles, which is a crucial factor for their successful adoption and deployment in society. Automated vehicles must be reliable in every possible driving scenario. This requires a strong safety argumentation, which still remains a significant challenge worldwide.
For higher levels of automation, case-by-case validation testing is not feasible due to the high number of scenarios involved. Public road validation is another option, but since conditions are uncontrollable, this option is ineffective and therefore expensive. For that reason, a mixture of physical and virtual testing has emerged as a promising approach. Virtual simulation allows for cost effective testing of large scenario volumes, although the reliability of the results is often compromised.
Worldwide, several initiatives have started to develop test- and assessment methods for automated vehicles, applying a scenario-based approach, and combining both physical and virtual testing. Although automotive stakeholders generally seem to agree on this overall approach, the current situation is leading to silo solutions. The lack of a common approach, therefore hampers the large-scale and safe introduction of automated vehicles in our society.
It is for these reasons that the SUNRISE project started. The SUNRISE project aims to establish a common safety assurance framework, interconnecting the silos and making them collaborate in a harmonized way.

## Slide 7
Main goal
* CCAM = Cooperative, Connected and Automated Mobility
Key facts
Run time Sep 2022 – Aug 2025
Budget 13.455.866,25 €
Develop and provide a harmonized and scalable CCAM* Safety Assurance Framework that fulfils the needs of different automotive stakeholders, for a continuously evolving number of use cases and scenarios.
Safety Assurance Framework
Developers
Researchers
Certifiers
Citizens
…
Key one-liner
“The decade long debate in scenario-based assessment, converges into a common basis.”
SUNRISE
Safety assUraNce fRamework for connected and automated mobIlity SystEms
Notes: SUNRISE stands for Safety assUraNce fRamework for connected and automated mobIlity SystEms.
The main goal of this project is to develop a harmonized and scalable CCAM Safety Assurance Framework that fulfils the needs of different automotive stakeholders. CCAM stand for Cooperative, Connected and Automated Mobility. This safety assurance framework plays a key role in the project. And as you can see in the image on this slide, different stakeholders each have their own specific interest in this safety assurance framework. For example, developers of CCAM systems, but also the entities that certify these systems, or that perform research in this field. And even citizens might have their own specific interest in this safety assurance framework.
Achieving the main goal shown on this slide, will accelerate the large-scale deployment of CCAM systems and the societal benefits that these systems bring along.
The runtime of this project is 36 months. It started in September 2022, and it will finish until August 2025. The total budget of this project is almost 13.5 million Euros , funded completely by the European Union.
A key one liner that I would like you to remember, since it best describes the SUNRISE project in the short and simple way , is the following: “The decade long debate in scenario-based assessment, now converges into a common basis.” That is what the SUNRISE project is all about: the conversion into a common basis, of the decade long debate on scenario based assessment. Take that with you!

## Slide 8
Vision
Researchers
How do I compare my automated vehicle test results to those of others?
Citizens
What to look for, when I buy an automated vehicle?
Certifiers
How should I assess the safety of automated vehicles?
Vehicle Developers
What scenarios should I test my automated vehicles for?
Safety Assurance Framework for Connected and Automated Mobility Systems
Project No. 101069573
Tool Developers
How can I make my tools fit those of others?
© SUNRISE
Notes: SUNRISE stands for Safety assUraNce fRamework for connected and automated mobIlity SystEms. But this is quite an abstract and intangible topic. In order to help you visualize the safety assurance framework being developed under SUNRISE, we created this image. Again, it shows the different types of stakeholders, that each have their own interests in the framework. It also shows possible questions that each of these stakeholders want to get answered by the framework (represented in this image by the big cloud).
Vehicle developers for example, are likely to ask what scenarios they should test their automated vehicles for. Certifiers will want to know, how they should assess the safety of automated vehicles. Researchers might want to know, how to compare their test results to those of other researchers. And tool developers might ask, how they can make their tools fit or interoperate with those of other providers.
The SUNRISE safety assurance framework aims to provide answers to these questions (among many others). It provides these answers, with the method, toolchain and data framework that it will develop (and demonstrate). And it does not operate independently. Instead, it cooperates with many similar initiatives around the world, in the field of CCAM safety assurance. For example by aligning its components with those of twin projects (like V&V Methods and Sakura), or by drawing contents from related scenario databases (like Street Wise or Safety Pool).

## Slide 9
Workplan
WP2
WP1 – Management
WP2 – Framework
WP3 – Method
WP4 – Toolchain
WP5 – Ontology
WP6 – Data framework
WP7 – Demonstration
WP8 – Cooperation
WP9 – Outreach
WP2
WP9
WP5
WP5
WP3
WP7
WP7
WP3
WP3
WP4
WP6
WP3
WP6
WP5
WP4
WP2
WP6
WP7
WP9
WP8
WP8
WP8
WP8
WP8
WP1
Notes: This slide shows the general approach or work plan applied in the SUNRISE project. Again, you can see a central role for the safety assurance framework. As shown in the upper left part, this framework is based on several Methods and a Toolchain. For example a method for scenario selection and allocation, and tools for physical and virtual evaluation. As shown in the upper right part, another important component is the Data Framework with its structure and governance mechanisms, as well as an ontology, laying the foundation for querying and interoperability. As you can see in the center part of this overview, the safety assurance framework will be put to the test by a series of relevant and realistic Test Cases
.
The development of the method, the toolchain, and the data framework, does not start from scratch. It is based on existing safety assurance frameworks and related initiatives (including the predecessor project HEADSTART), as can be seen in the upper part of this workplan. The Test Cases are derived from a variety of CCAM systems and Use Cases, including urban- and highway driving of passenger cars, but also automated parking of freight vehicles.
The bottom part of this workplan shows the technical results and demonstrators, including a CCAM safety assessment method and toolchain, but also an interactive user handbook, and an EU data framework including a scenario database and test case library.
Together with twin initiatives from other parts of the world (such as V&V Methods and Sakura), the SUNRISE consortium actively engages with external stakeholders, such as vehicle safety bodies (like UNECE and EuroNCAP), as well as standardization entities (like ISO, SAE and ASAM). This engagement aims at adoption of project results by these external stakeholders.

## Slide 10
What’s new?
Methodologies
Harmonization Standardisation
Environmental conditions
Simulation platform
Use cases
Toolchain
Type approval scheme
International cooperation
Coverage
Extend
Create
Improve
Future proof
Mixed traffic
Edge cases
Scenario sharing &
database principles
European Data Framework
HEADSTART
SUNRISE
CCAM Safety Assurance Framework
TRL 3-4
TRL 6-7
Notes: This slide shows “what’s new” in the SUNRISE project. This project does not start from scratch: it is based on predecessor project HEADSTART, which finished early 2022. As this slide shows, based on the methodologies and harmonization efforts performed in HEADSTART, SUNRISE will work towards the establishment of a broader CCAM Safety Assurance Framework.
In green, this overview shows the items that already started under HEADSTART, and will be improved under SUNRISE. These are items like methodologies, harmonization, standardization and international cooperation.
In orange, you see the items that will be considerably extended under SUNRISE, with respect to HEADSTART. The number of use cases for example, will be significantly increased. SUNRISE will also put more emphasis on topics like environmental conditions, mixed traffic and edge cases. And it will also focus much more on the toolchain, and specifically on virtual simulation.
In red you can see those items that are completely new under SUNRISE, and which didn't exist in HEADSTART. We will create for example, the first version of an European scenario database, as part of a data framework with its scenario sharing and database principles. We will also create the first version of a type approval scheme that can be used by regulating entities. Furthermore, we will make sure that the framework is future proof, which means that future technologies can also be addressed by our framework. All these items are part of the safety assurance framework that will be developed under SUNRISE.
Another important aspect to take into account, is that HEADSTART worked on a different technology maturity level. HEADSTART worked on a technology readiness level (TRL) of 3 to 4, whereas under SUNRISE, this technology readiness level (TRL) will be raised to 6 or 7. This means that the technology becomes more mature under SUNRISE. We will demonstrate a working prototype, for example. So, under SUNRISE, results get much closer to their final application by its users.

## Slide 11
Partners
+ External Experts
+ Related initiatives
Notes: The SUNRISE project counts with a total of 22 consortium partners from a variety of European Member States. The different types of stakeholders that each have their specific interest in the safety assurance framework , are reflected in this consortium. As this slide shows, the SUNRISE consortium includes entities from the areas of research, technology development, tool development and certification, which corresponds to the main stakeholders interested in SUNRISE results.

## Slide 12
Partners

## Slide 13
Team
SUNRISE team members
General Assembly San Sebastian Oct 2024

## Slide 14: SUNRISE Safety Assurance Framework
ccam-sunrise-project.eu
27 November 2024
John Fredrik Grönvall - Chalmers Industriteknik
Jason Zhang - Warwick University

## Slide 15
SUNRISE Safety Assurance Framework

## Slide 16
ODD & Behaviour, External Requirements, Test Objectives
Safety Performance Assurance
SUNRISE scope
In Service Monitoring and Reporting (ISMR)
Audit
SUNRISE Safety Assurance Framework
Notes: At a high level, there are three main components of the safety assurnace framework, which are Audit, in-service monitoring and reporting (or ISMR), and performance assurance. The performance assurnace focuses on ensuring that the system can performance as intended within its defined Operational design Domain (or ODD, which can be visualised as a set of operating conditions within which the system is designed to opérate safely). The Audit focuses on ensuring the development process, the tolos used, as well as the management system are adequte. And the ISMR focuses on capture and record any additional information during hte system deployment for consideration into the system’s future design.
2. All components are part of Ssafety assurance framework, however in SUNRISE we focus on the performance assurnace using a scenario based approach, and incorpórate virtual environment.
Please note that We also have the Input layer to the Safety assurance framework, which includes the requirments containing ODD & behaviour, as well as other external requirements and test objectives.

## Slide 17
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 18
Scenario
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 19
Execute
Scenario
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 20
Execute
Scenario
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 21
Create
Execute
Scenario
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 22
Create
Execute
Scenario
Format
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 23
Create
Execute
Scenario
Format
Store
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 24
Create
Execute
Scenario
Format
Store
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 25
Create
Execute
Scenario
Format
Store
Allocate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 26
Create
Execute
Scenario
Format
Store
Allocate
Execute
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 27
Create
Execute
Scenario
Format
Store
Allocate
Execute
Coverage
Test Evaluate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 28
Create
Execute
Scenario
Format
Store
Allocate
Execute
Coverage
Test Evaluate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 29
Create
Execute
Scenario
Format
Store
Allocate
Decide
Execute
Coverage
Test Evaluate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 30
Create
Execute
Scenario
Format
Store
Allocate
Decide
Execute
Coverage
Test Evaluate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 31
Create
Execute
Scenario
Format
Store
Allocate
Decide
Execute
Coverage
Test Evaluate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 32
Create
Execute
Scenario
Format
Store
Allocate
Decide
Execute
Coverage
Test Evaluate
Analyse
Audit
In Service Monitoring and Reporting (ISMR)
ODD & Behaviour, External Requirements, Test Objectives
Query & Concretise
SUNRISE Safety Assurance Framework
Notes: Now let us have a look at what are the main building blocks of the performance assurance workflow. At a high level, it contains scenario, execute, and analyse. Essentially, it means that to conduct the safety assurance process, we only need a set of scenarios, an environment for executing the scenarios, and a process to analyse the execution result in order to determine whether the system is safe or not. The scenario building block further contains create, format and store. Create talks about the creation of scenarios. During the benchmarking stage, we identified two different approaches for the scenario creation, which are knowledge based approach, and data based approach. An example of a data based scenario creation approach is to create scenarios using accident dataset, such as the UK STATS 19 accident dataset. An example of a knowledge based scenario generation approach is to use an expert’s domain knowledge to identify weak points within a system, therefore creating scenarios to explore such weakness. Once the scenario contents are created, the next stage is to format it into a specific format to represent the scenario. Considering the multiple stakeholders involved in a scenario based testing workflow, such as regulators, research engineers, test engineers, system engineers, the public, there is a need to use multiple abstraction levels for the scenario format. During the benchmarking stage, we identified 4 levels of scenario abstractions, they are functional level scenarios, abstract level scenarios, logical level scenarios, and concrete level scenarios. Each level focus on different properties, for example functional and abstract levels may focus on human readability, whereas logical and concrete levels may focus on machine readability. We also identified the importance of using common format, such as the ASAM OpenSCENARIO and OpenDRIVE formats for the logical and concrete levels representation; And the BSI Flex 1889 for abstract level scenario representation. Once the scenarios are created and formatted, the next step is to store them in a scenario database for downstream testing activities. During the sunrise project, we propose a common Federated layer of accessing multiple scenario databases. We identified requirements for such databases to be connected to the sunrise Federated layer. The scenario creation and formatting will then become the responsibility of individual database owners. However it is also their responsibility to ensure that the requirements are met in order to be able to connect their own databases to the Federated layer, such as using common scenario format and incorporating multiple abstraction levels. So far, the create format and store have covered the complete scenario block. Within the execute block, we have concretize, allocate, and execute. The concretize takes input from the input layer which contains ODD behaviour, external requirements and test objectives. It then passes such requirements to the sunrise Federated layer as a query, and obtains scenarios from the Federated layer which further queries scenarios from the individual scenario databases. Please note that such returned scenarios, back from the Federated layer to the concretise, are of the form of logical scenario, which means all the parameters are defined using value ranges, so it means that infinite numbers of concrete scenarios can be derived from one such logical scenario. Therefore, the next task the concretize will do is to concretize such parameter ranges into specific concrete values, and to combine the concrete scenarios with the test objectives. Once such concrete scenarios and test objectives are combined, the next step is to allocate them within an execution environment. To execute a scenario, the sunrise safety assurance framework allows all possible environments to be used, therefore it is environment agnostic. Such environment ranges from full virtual environment, through to simulated environment such as vehicle or hardware in the loop, through to controlled environment for real world testing, and to public road. Work package 3 will develop a test environment allocation workflow, which will be later implemented within the wider safety assurance framework. After the environment is allocated, the next step is to execute such scenario and record the corresponding execution data. Once we have the execution data, we need to conduct the corresponding analysis to determine whether the system is safe or not. There are two main steps within such analysis, one is called coverage analysis, and the other one is called test evaluation. The coverage analysis utilising a multi pillar approach, looking at the test from multiple interested angles or perspectives, and working out a combined coverage outcome. Search perspectives could include analysing the coverage of the parameter value ranges as defined in the logical scenario by the individual concrete parameter values, Please note that there is an iterative process to constantly derive new concrete scenarios within a given logical scenario parameter ranges based on the outcome of the analysis block, in order to identify the failure conditions (i.e., those parameter combinations that result into system failure), this feedback loop is indicated by the red feedback arrow, and will be covered very shortly. The other example aspect of the coverage can be the ODD analysis, for example, we could look at the accumulated ODD features that are covered from the set of test scenarios, and decide whether we have covered enough of the system’s ODD with this set of test scenarios. The reason why we focus on ODD so much is that the operational design domain of a system is the operating boundary which the system developer claims it can operate safely. Therefore it is our job to fully explore such claimed operating boundary using a diverse enough set of scenarios. These are just two examples that form such coverage concept, sunrise project will explore the coverage analysis concept further in the future stage of the project. The other building blocks of the analysis part is the test evaluate, this block looks at individual test execution, evaluates whether the system has passed or failed individual test execution. For example, whether the system has successfully stayed under an upper limit of certain speed requirement, or whether the system has successfully avoided collisions. Both the coverage analysis and the test evaluation will fit into the overall analysis block and the result will be used to create further concrete parameters within the original scenario using parameter ranges. After many iterations, once coverage analysis has reached the threshold, the coverage result combined with the test evaluation result will be fed into the decide block and produce the whole safety assurance outcome of the system.

## Slide 33: Questions from audience
ccam-sunrise-project.eu
27 November 2024
Stefan de Vries - Applus IDIADA
Jason Zhang - Warwick University
John Fredrik Grönvall - Chalmers Industriteknik

## Slide 34
ccam-sunrise-project.eu
Horizon Research and Innovation Actions | Project No. 101069573
SUNRISE Cooperation Platform
27 November 2024
Stefan de Vries - Applus IDIADA
Jason Zhang - Warwick University
John Fredrik Grönvall - Chalmers Industriteknik

## Slide 35: Thank you and stay safe!
27 November 2024
Stefan de Vries - Applus IDIADA
Jason Zhang - Warwick University
John Fredrik Grönvall - Chalmers Industriteknik
ccam-sunrise-project.eu
Horizon Research and Innovation Actions | Project No. 101069573